## Slide 1
표지
May 2019
Park, Hye Sook
National Meteorological Satellite Center
Korea Meteorological Administration
Current status of S-band Weather Radar Network in Korea
All contents credit by Seung-Hwa Jung
In Weather Radar Center/KMA
Bilateral Cooperation between KMA and BoM(April 29th - May 3rd , 2019, Australia)
Notes: This time, I am going to talk about what has been changed in weather radar network in terms of ground validation of space borne radar.

## Slide 2
Contents
Improvement of data processing chain
New Scanning Strategies : Low level coverage
Radar-QPE Technique : Hybrid Surface Rainfall
Notes: I will mention about three topics; update cycle of radar, low level coverage, and radar rainfall estimation

## Slide 3
Weather Radar Network of KMA
- Deployment along the national boundary
: wide observational coverage
- installation on the top of a mountain (max > 1.0km)
: to avoid beam blockage
- wide observational range (> 240km)
- 10 minute update cycle
- volume scan ( 9 ~ 12 elev. angles)
KMA operational weather radar network
- 10 S-band Dual-Polarization radar
 issues : lazy update cycle, bad radar coverage at low altitude (<1km)

## Slide 4
Conventional data processing chain
time
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
Volume scan
(7min)
QC
(2min)
Mosaic
(6min)
Volume scan
(7min)
QC
(2min)
Mosaic
(6min)
Volume scan
(7min)
QC
(2min)
Mosaic
(6min)
Improvement of Data Processing Chain
What has been changed?
Scanning interval : 10 minutes  5 minutes
Single observation range (240km) over all volume scan
 the observation range decreases as function of elev. Angle  High PRF  faster scan
The number of elevation angles : 8 ~ 11  9 elevation angles
Employment of negative (-) elevation angle

## Slide 5
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
Conventional data processing chain
time
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
Volume scan
(7min)
QC
(2min)
Mosaic
(6min)
Volume scan
(7min)
QC
(2min)
Mosaic
(6min)
Volume scan
(7min)
QC
(2min)
Mosaic
(6min)
New data processing chain
time
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
Volume scan
(4min 30sec)
QC
(10sec)
Transfer sweep data
(every 30sec)
HSR1
(30sec)
HSR2
(30sec)
Volume scan
(4min 30sec)
QC
Transfer sweep data
(every 30sec)
HSR1
HSR2
Volume scan
(4min 30sec)
QC
Transfer sweep data
(every 30sec)
HSR1
HSR2
Volume scan
(4min 30sec)
QC
Transfer sweep data
(every 30sec)
HSR1
HSR2
Volume scan
(4min 30sec)
QC
Transfer sweep data
(every 30sec)
HSR1
HSR2
Volume scan
(4min 30sec)
QC
Transfer sweep data
(every 30sec)
HSR1
HSR2
Improvement of Data Processing Chain

## Slide 6
Contents
Improvement of data processing chain
New Scanning Strategies : Low level coverage
Radar-QPE Technique : Hybrid Surface Rainfall
Notes: I will mention about three topics; update cycle of radar, low level coverage, and radar rainfall estimation

## Slide 7
 | JNI | PSN | KWK | GDK | KSN
Lowest elev. angle [°] | -0.1 | -0.1 | -0.2 | -0.4 | 0.0
Determination of Lowest Elevation Angle
Beam blockage simulation with high vertical resolution (0.1ᵒ)
From W. Krajewski, Univ. of Iowa
high vertical resolution (0.1ᵒ)
digital elevation model with 1”
standard refraction
two-way gaussian beam pattern
KSN
GDK
30%
30%

## Slide 8
Existing scanning strategies (10 min)
New scanning strategies (5 min)
Lowest Observable Height
[%] | SSP | GNG | GSN | BRI | KSN | JNI | GDK | KWK | GDK | MYN
Existing | 6.4 | 5.2 | 7.1 | 12.6 | 5.7 | 12.3 | 2.7 | 2.0 | 0.0 | 0.0
New | 10.3 | 7.8 | 12.9 | 14.9 | 9.0 | 14.7 | 10.5 | 11.4 | 4.8 | 9.1
Diff. | +3.9 | +2.6 | +5.8 | +2.3 | +3.3 | +2.4 | +7.8 | +9.4 | +4.8 | +9.1
Low Level Radar Coverage (<1km) : 15.8%  39.8%

## Slide 9
Old strategy
1400KST at 30th January, 2018
New strategy
Elev : 0.3ᵒ
Elev: -0.2ᵒ
1500KST at 30th January, 2018
Benefit of New Scanning Strategy
radar coverage at low altitude (<1km) enlarged

## Slide 10
Contents
Improvement of data processing chain
New Scanning Strategies : Low level coverage
Radar-QPE Technique : Hybrid Surface Rainfall
Notes: I will mention about three topics; update cycle of radar, low level coverage, and radar rainfall estimation

## Slide 11
Rainfall Estimation Technique based on Hybrid Surface
: the rainfall estimation technique base on the lowest-observable elevation surface, in radar volume scan that immunes to radar beam blockage, ground clutter contamination and non-meteorological echoes
Blocking
Ground
Clutter
Chaff
blockage fraction＜10%
avoiding non-rain echo
Ground Echo(GRE) Identification
by applying threshold of
(DZ-CZ), RH, STDEV(DZ), STDEV(CZ)
2017/08/15 06:30KST
PPI0
PPI0
sea clutter
BRI
ground clutter
Hyb.
BRI
2017/06/01 14:10KST
PPI0
chaff
ground clutter
MYN
Hyb.
MYN
Hybrid Surface Rainfall

## Slide 12
강우추정을 위한 이중편파 레이더 변수
Identification of ground clutter
Classification of Non-meteorological echo
Blockage simulation
Construction of Hybrid Surface
Hybrid Surface[°]
Height of Hybrid surface [km]
Hybrid Surface Rainfall

## Slide 13
Identification of ground clutter
Classification of Non-meteorological echo
Blockage simulation
Construction of Hybrid Surface
Hybrid Surface Rainfall
If ＞45dBZ & ＞1.3°/km,
else if＞15dBZ ＞0.2dB,
DSD data of 2DVD from April 2014 to Oct. 2017

## Slide 14
Blocking area
due to Mt.Halla
→ Huge
observation gap
PPI0
HSR
SSP, Typhoon ‘Chaba’ (2016.10.04~05)
Example of Hybrid Surface Rainfall
QPE is also improved by hybrid surface technique
not only in observation gap due to ground clutter but also in beam blockage area.

## Slide 15
Summary and future works
Scanning strategies : 10minutes  5 minutes
We applied to negative (-) elevation angle
 radar coverage (< 1km height): 18.5%  39.8%
Volume-based data processing chain  sweep-based data processing chain
 Service time has been dramatically reduced (15 min  3 min)
KMA’s operational radar-QPE has been changed from PPI and CAPPI to Hybrid Surface Rainfall (HSR)
 QPE performance : 51.8%  75.5%
Notes: The result of QPE verification of 2017 is also similar to previous result.
QPE is also improved by hybrid surface technique not only in observation gap due to ground clutter but also in beam blockage area.

## Slide 16
Thank you for your attention