## Slide 1: An introduction of Japanese new geostationary meteorological satellite, Himawari-8
Meteorological Satellite Center of JMA
Tasuku TABATA

## Slide 2
Himawari-8 began operation
at 02:00 UTC on 7th July 2015.

## Slide 3
Outline of Himawari-8
Data Distribution/dissemination Method
Enhancement in Himawari-8 Geophysical Products
Contents

## Slide 4
Outline of Himawari-8

## Slide 5: Outline of Himawari-8
Geostationary position | Around 140.7° E
Attitude control | 3-axis attitude-controlled geostationary satellite
Communication | 1) Raw observation data transmission Ka-band, 18.1 - 18.4 GHz (downlink)
 | 2) DCS International channel 402.0 - 402.1 MHz (uplink) Domestic channel 402.1 - 402.4 MHz (uplink) Transmission to ground segments Ka-band, 18.1 - 18.4 GHz (downlink)
 | 3) Telemetry and command Ku-band, 12.2 - 12.75 GHz (downlink) 13.75 - 14.5 GHz (uplink)
solar panel
communications antennas
Advanced Himawari Imager (AHI)
 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
MTSAT-1R MTSAT-2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Himawari-8 Himawari-9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
standby
manufacture
manufacture
a package purchase
launch
standby
launch
operation
operation
operation
standby
operation
standby
standby
standby
Himawari-8 began operation on 7 July 2015, replacing the previous MTSAT-2 operational satellite

## Slide 6: Advantage of AHI
３０min.
１０min.
VIS 1 km
IR 4 km
Improved spatial resolution
More spectral bands
More frequent observation
More flexible regional observation
Special
observation
Target area obs. every 2.5 minutes
１０min.
１０min.
G
B
R
VIS 0.5/1 km
IR 2 km
MTSAT-1R/2
Himawari-8/9
5 bands
16 bands
10 bands
3 bands
3 bands
IR
4 bands
NIR
1 band
IR
VIS
VIS

## Slide 7: Characteristics of AHI 16 Spectral bands
RGB band
Composited
Water vapor
Atmospheric
Windows
SO2
O3
CO2
0.51 µm (Band 2)
instead of ABI’s 1.38 µm
True Color Image
VIS
IR1
IR2
IR3
IR4
as of MTSAT-1R/2
Band | Wavelength [µm] | Quantization [bit] | Spatial Resolution (km)
1 | 0.46 | 11 | 1km
2 | 0.51 | 11 | 1km
3 | 0.64 | 11 | 0.5km
4 | 0.86 | 11 | 1km
5 | 1.6 | 11 | 2km
6 | 2.3 | 11 | 2Km
7 | 3.9 | 14 | 2Km
8 | 6.2 | 11 | 2Km
9 | 7.0 | 11 | 2Km
10 | 7.3 | 12 | 2Km
11 | 8.6 | 12 | 2Km
12 | 9.6 | 12 | 2Km
13 | 10.4 | 12 | 2Km
14 | 11.2 | 12 | 2Km
15 | 12.3 | 12 | 2Km
16 | 13.3 | 11 | 2Km
Similar to ABI for GOES-R

## Slide 8: Dawn of a “New Era”
02:40 UTC on 18 December 2014
MTSAT-2
Hourly in Monochrome
Himawari-8
every 10 minutes in Full-Color
April 2, 16UTC - April 3, 13UTC

## Slide 9: Advantage of Resolution
MTSAT-2 (1km)
03:00 UTC on 29 January 2015
Visible Band
Himawari-8 (0.5km)
Tokyo
Tokyo

## Slide 10: Advantage of many spectral bands
Combination of B11, B13 and B15
Mt. Raung volcano, in Indonesia
Shimizu-san will lecture particularly about RGB in next term.